## Slide 1: Smart traffic signals from entrance counts
Simulate → forecast → estimate the queues → optimise → measure wait time
Senior Quant case study · Problem 1: smart traffic-light optimisation
Glen McKenzie
Notes: Opening (20 seconds). The project is a full loop: I built a vehicle-level traffic simulator, a forecaster for arrivals at each entrance, a queue estimator, and a convex optimiser that sets the green splits every minute. Everything is judged on one number, average delay per car, on days the controller was never tuned on. The key assumption, which I'll come back to: the controller only sees a car counter on each road into the network. Nothing inside. So it has to predict and estimate, which is the point of an ML-plus-optimisation case.

## Slide 2: A third less waiting than a tuned fixed plan on a normal morning
THE ANSWER UP FRONT
32%
less delay per car than a tuned fixed green wave on a typical morning (10 held-out days, 72 → 49 s)
43–64%
less than the untuned 60 s fixed plan, in every one of the six scenarios
7.1%
forecast error, 15 min ahead, vs 10.4% for the hour-of-day profile and 24% for the raw count
≈ 0 s
what the learned forecast adds to delay over repeating the last count. The gain is in the queue model and the optimiser
The brief's success criteria
Criterion | Status | Evidence
20%+ less delay than fixed timing | Met vs untuned; partly vs tuned | 43–64% vs the 60 s plan everywhere; vs the tuned plan 32% typical and 22% busy mornings, 5–15% in storm, evening, accident and event
4+ intersections | Met | 2x2 grid evaluated; the same code solves a 10x10 (100 junctions) in 1.9 s per decision
Real-time visualisation | Met | Side-by-side viewer: fixed plan vs optimiser on identical traffic, five clips, estimate vs truth
Responds to accidents and closures | Met, with a fallback | Incident feed + fallback to the tuned plan; also scheduled events via the calendar
Notes: The headline: on a normal morning the optimiser cuts delay per car by about a third against a fixed green wave whose cycle I tuned as well as I could. Against the kind of untuned plan the brief probably means by "fixed timing", it's 43 to 64 percent better in every scenario. The honest part, which I'll keep coming back to: the learned forecast is a good forecast, but it adds almost nothing to delay. Persistence, my model, and a perfect oracle forecast all give about the same delay. The gain comes from the queue model and the optimiser. I'll show why. Criteria: 20% is met against the untuned plan everywhere, and against the tuned plan only on the typical and busy mornings. The tuned baseline is deliberately strong.

## Slide 3: Plan with a simple model, get judged in a detailed one
THE PIPELINE
Simulator
Vehicle-level, 0.5 s steps. Owns the truth: real queues, real demand
Forecaster
Poisson GLM: arrivals at each entrance for the next 15 min
Queue estimator
Store-and-forward model fed by the counts and its own signals
Optimiser
Convex QP every 60 s: green splits for the next 15 min; Webster cycle
Signals
Executed second by second, with gap-out and incident fallback
entrance counts
15-min arrivals
cars per road
green shares + cycle
the simulator moves the cars under those signals; delay per car is measured on the simulator's truth
Why two models?
The controller's store-and-forward model is cheap and linear, so it can be optimised exactly. The simulator is detailed, so the score includes the error of that simpler model (start-up loss, spillback, rain).
What is learned vs. modelled?
Learned: the arrival rate (from 60 days of history). Modelled: how queues form and drain (physics we know). Optimised: the green splits.
Judged on
Mean delay per car on held-out days (seeds never used for any choice), against a fixed plan whose cycle was tuned on each scenario's normal day.
Notes: This is the whole system on one slide. The simulator owns the truth. The controller only sees counts at the entrances. The forecaster turns those counts into expected arrivals for the next 15 minutes, the estimator turns counts plus its own signal history into cars per road, and the optimiser uses both to pick green splits. Then the simulator moves the cars and I measure delay. The design choice I want to flag: the controller plans with a deliberately simple linear model, but it is graded in a much richer simulator. If I graded it in its own model it would look perfect. The gap between the two models is part of the test.

## Slide 4: Why a vehicle-level simulator, and why time-stepped
1 · SIMULATION
SIMULATION
FORECASTER
OPTIMISER
RESULTS
Option | What it gives | Why not chosen / why chosen
Score in the controller's own store-and-forward model | Fast, exact, already written | The controller would be graded on its own assumptions: no start-up loss, no spillback dynamics, no model error. Rejected.
Cell-transmission (macroscopic flow) model | Spillback, fast | Still a flow model: queue discharge is an input, not an outcome. Rejected.
SUMO or a commercial micro-simulator | Realistic, validated | Heavy dependency, slow to set up and make reproducible in a weekend, harder for a reviewer to read. Rejected.
Event-driven (queue) simulation | Exact timing, fast in light traffic | Needs a queueing abstraction: it assumes the service process we want to observe. Rejected.
Own time-stepped car-following simulator (IDM, Δt = 0.5 s) | Queues, saturation flow, start-up loss, spillback and rain effects all emerge from driver behaviour | Chosen. Cost: we must calibrate and test it ourselves (12 simulator tests: conservation, no overlap, saturation flow, rain, accidents, common random numbers).
The principle
The controller should never be graded in the model it plans with. The simulator is richer than the controller's model, so every result includes model error, as it would on a real street.
Why 0.5 s steps
A ballistic IDM update at 0.5 s is the standard scheme (Treiber & Kesting): it resolves stop-and-go waves and the 4 s amber. Cheap: 20 simulated minutes on the 2x2 take 0.3 s under the fixed plan, 1.1 s with the optimiser.
Notes: The first decision was how to score. The tempting shortcut is to evaluate the controller in the same queue model it optimises over. That is grading your own homework: no model error by construction. So I wrote a vehicle-level simulator. Every car follows the Intelligent Driver Model, which is the standard car-following model in the literature (Treiber 2000). Saturation flow, start-up delay, spillback and the rain effect are not parameters I set: they come out of the driving behaviour, and I measure them. Why not SUMO? It is the real tool, but in a weekend it's a big dependency and harder for you to read and reproduce. Why time-stepped and not event-driven? Event-driven needs a queue abstraction, which assumes exactly the service process I want to observe. If asked about step size: 0.5 s is the usual choice for IDM with a ballistic update. It's fast enough: 20 simulated minutes take 0.3 s under the fixed plan.

## Slide 5: Network and vehicles: small enough to read, rich enough to congest
1 · SIMULATION
SIMULATION
FORECASTER
OPTIMISER
RESULTS
200 m internal (~30 cars)
400 m entry roads (~61 cars), counter at the boundary
2x2 grid · 4 junctions · 16 links · 8 entries, 8 exits
Assumption | Value | Why
Lanes, phases | 1 lane per approach; 2 phases (NS / EW) | Smallest setting with real conflicts; turns share the lane
Turns | 70% straight / 15% left / 15% right, drawn per car | Survey-style averages the controller also knows
Signal timing | 4 s lost per switch; green 8–60 s | Amber + all-red; standard minimum and maximum green
Car | 4.5 m + 2 m gap = 6.5 m queued | Storage per road follows from length
Car following (IDM) | v₀ 13.9 m/s (50 km/h), T 1.5 s, a 1.5, b 2.0 m/s², s₀ 2 m | Urban values from Treiber & Kesting
Saturation flow | 0.40 veh/s (1,440/h); 0.33 in full rain | Emergent from IDM, measured and tested, not set
Junction rules | Dilemma-zone amber; box-clearing; full entry road → cars wait outside | Realistic spillback; waiting outside counts as delay
Not modelled | Lane changes, pedestrians, protected turns, rerouting | Out of scope; listed as limitations
Notes: The network is a 2x2 grid: four junctions, eight roads in, eight out, four internal roads. One lane each way, two signal phases, north-south and east-west. Every car draws its turns when it is created: 70% straight, 15% left, 15% right. Internal roads are 200 m, which holds about 30 queued cars. Entry roads are 400 m, about 61 cars. That matters later: when an entry road is full, cars wait outside the network, and the counter at the boundary stops seeing them. That's censoring, and it causes trouble for both the forecaster and the estimator. The car-following parameters are standard urban values. Saturation flow is measured, not set: about 0.40 cars per second per lane, 1,440 per hour, which is in the usual range for one urban lane. Rain lowers it to 0.33. Small details that make congestion realistic: an amber dilemma-zone rule, and box-clearing: a car won't enter the junction if there's no room on the road ahead. That's what produces spillback. Why 2x2? It's the smallest grid with interaction between junctions, and everything is generated from the grid size, so 10x10 is a config change.

## Slide 6: Demand: Poisson arrivals around a hidden, structured rate
1 · SIMULATION
SIMULATION
FORECASTER
OPTIMISER
RESULTS
λₑ(t) = 0.136·P(h−δ)·L·(1+0.1r)·(1+0.25τdₑ)·e^εₑ·(1+Sₑ)
arrivals at entry e ~ Poisson(λₑ(t)): a doubly stochastic (Cox) process
Term | What it is | Can a forecaster learn it?
0.136 | 0.16 veh/s (the grid's saturation knee) × 0.85: a normal peak runs at 85% of capacity | Constant
P(h − δ) | Weekday profile: AM peak 07:42, PM 17:00, midday plateau; δ = today's timing shift, sd 12 min | Profile from history; shift from today's counts
L | Today's level, lognormal, sd 10% | From today's counts
1 + 0.10 r | Rain intensity r (0 to 1) adds up to 10% demand | From the weather feed
1 + 0.25 τ dₑ | Tide: inbound-heavy AM, outbound-heavy PM (dₑ = ±1 by direction) | Profile × entry
e^ε | AR(1) noise per minute, φ = 0.9 (~10-min memory): shared + half-size per entry | Partly, from recent counts
1 + Sₑ | Scheduled event surge on one side; announced size × lognormal(0, 0.25) | Announced part from the calendar
Poisson | Count noise: a 5-min count of 30–90 cars carries 10–20% pure noise | Never
Designed in layers
Each layer is something a forecaster could learn from history, from today's counts, from a feed, or not at all. That makes the forecast ladder interpretable.
Notes: Demand is the part I designed most carefully, because it decides what the forecaster can possibly learn. The rate at each entrance is a product of layers. A weekday profile with morning and evening peaks. A timing shift: today's rush might come 12 minutes late. A day level: today might be 10% busier. Rain adds up to 10%. A directional tide: inbound in the morning, outbound in the evening. Slow AR(1) noise with about ten minutes of memory. And scheduled events. Arrivals are Poisson around that rate, so it's a Cox process: the rate itself is random. The 0.136: 0.16 cars per second per entry is where the grid saturates under fixed timing; a normal peak runs at 85% of that. Why multiplicative? Real traffic effects scale: rain or a busy day raise every hour proportionally. And it makes a log-link model the natural forecaster. Each layer has a different answer to "can it be learned": the profile from history, the level and shift from today's counts, rain and events from feeds, Poisson noise never. That's why the forecast ladder later reads cleanly. If asked how I chose the Poisson parameters: Poisson has one parameter, the rate. The choice is the rate model above. The noise sizes (10% level, 12-min shift, AR sd) are assumptions chosen to give a 12-20% day-to-day spread at the same time of day, shown in the lower panel. They are not calibrated to real data, and I say so.

## Slide 7: Disturbances, random days, and the six test scenarios
1 · SIMULATION
SIMULATION
FORECASTER
OPTIMISER
RESULTS
Random days (forecaster history, 60 days)
Draw | Assumption
Day level, timing shift | Lognormal sd 10%; shift sd 12 min
Storms | Poisson ~0.8/day, 70% start 13:00–19:00. Free speed −20%, headway +30%, accel −15% → saturation flow −17%
Accidents | Poisson 0.10/h (×3 in rain): one lane blocked 15 min, no rerouting
Scheduled events | Poisson 0.4/day, 11:00–20:00, 20–90 min, random side; announced +40% to +120%; actual = announced × lognormal(0, 0.25)
All rates are assumptions, not calibrated to a city. Events use their own random stream, so adding them left every other day unchanged.
Evaluation scenarios (3 hours each)
Scenario | What happens | Tests
Typical morning | 06:00–09:00 normal weekday | The everyday case
Busy morning | Same, demand +15% | Near saturation
Storm | Rain across the peak | Capacity drop the model must track
Accident | One lane blocked 07:42–07:57 | Closures (brief criterion)
Typical evening | 15:30–18:30, outbound tide | A different peak
Stadium event | West side lets out 16:15: two eastbound entries double for 45 min | Where a forecast should matter
Why these scenarios
Each one stresses a different link of the chain: the busy morning stresses capacity, the storm the estimator's discharge assumption, the accident the incident path, and the stadium event the forecaster (information that arrives before the cars do). Baselines are tuned on the normal day only, so disturbed days test robustness, not tuning.
Notes: Two kinds of randomness. Random days, used to build 60 days of history for the forecaster: each day draws its level, timing shift, storms, accidents and events. And six fixed evaluation scenarios, each three hours. The scenarios are chosen to stress different parts of the chain. Busy morning: capacity. Storm: saturation flow drops 17%, which the estimator has to know about from the weather feed. Accident: the brief's closure criterion. Evening: a different peak with outbound tide. And the stadium event, which I added specifically as the case where forecasting should pay: the calendar announces the crowd before the cars arrive. All the rates are assumptions. I didn't have real data; I chose values that give plausible variability and I say that plainly in the limitations.

## Slide 8: What the controller is allowed to know: counts only
1 · SIMULATION
SIMULATION
FORECASTER
OPTIMISER
RESULTS
It sees
A car counter on each of the 8 entry roads (cumulative count)
The clock and calendar (weekday / weekend)
A weather feed: rain now and a noisy rain forecast
An incident feed: “road X blocked”, then “cleared”
An event calendar: time, side and announced crowd size
Its own signal states
The map: road lengths, average turn shares, nominal saturation flow
It never sees
Queues or cars on any road (no cameras, no stop-line detectors, no occupancy)
Cars waiting outside a full entry road
The true arrival rate
The actual size of an event crowd
Which way each car will turn
Enforced in code
The controller receives a filtered observation. A test hands it only the allowed keys; reading count, queue, spill or entry occupancy raises an error.
True rates are used only as forecast labels (a stand-in for a historical survey) and for scoring.
Why counts only (and not cameras)?
Practical: loop counters at the boundary are what most cities already have.
On theme: with cameras on every road, each junction could be run on observed queues and there is little to predict. Counts only makes control an estimation and prediction problem.
Cost checked: an earlier camera version read the true queues. Counts only did no worse (typical morning 22% → 30% better than tuned, storm 16% → 15%).
Notes: This is the assumption that shapes everything else. The controller sees a counter on each road into the network, the clock, the weather, an incident feed, an event calendar, and its own signals. It never sees a queue. Why? Two reasons. Practical: loop counters are common infrastructure. And thematically: I first built it with cameras that read the true queue on every road. With that, the problem is much less interesting: you can run each junction greedily on what it sees, and there's nothing for the ML to do. Counts only forces the system to predict arrivals and estimate the state, which is what an ML-plus-optimisation case is about. It cost nothing: the counts-only optimiser is as good as or better than the camera one, because the model-based gap-out turned out to be strong. It's enforced by a test: the controller is handed an observation with only the allowed keys. Likely question: "isn't the event calendar cheating?" No: it publishes the announced crowd, not the real one, and the real crowd varies by 25%.

## Slide 9: Measurement: one metric, paired comparisons, untouched seeds
1 · SIMULATION
SIMULATION
FORECASTER
OPTIMISER
RESULTS
Metric: mean delay per car
Delay = time from the car's creation to exit − distance / free speed. It includes time waiting outside a full entry road and cars still in the network at the end; the first 300 s are discarded. Also reported: 95th percentile, worst entry, throughput, spillback.
Baselines (deliberately strong)
Untuned fixed: 60 s cycle, equal splits, green-wave offsets. What “fixed timing” usually means.
Tuned fixed green wave: cycle tuned on each scenario's normal day: 120 s morning, 180 s evening. Applied unchanged to busy, storm, accident and event days.
Max-pressure was tried in the camera version and lost everywhere (backup slide).
Seeds and what they are used for
0–59 + 5000+
forecaster history and fresh days
100–109
tuning: baselines, optimiser settings, fallback
200–209
held-out evaluation (never tuned on)
300
demo clips
Common random numbers
Each car's arrival time and turns are drawn at creation from per-purpose seeded streams, so for a given scenario and seed every controller faces exactly the same cars. Comparisons are paired by seed; intervals are 95% t-intervals on the per-seed saving (10 seeds; 3 for busy and storm). The stadium event was added after every setting was frozen.
Notes: One metric: average delay per car, measured from when the car is created, so waiting outside a full entry road counts. Cars still in the network at the end are included, which stops a controller looking good by holding cars back. Two baselines. The untuned 60 s plan is what most people mean by fixed timing. The tuned green wave is my strong baseline: I tuned its cycle on each scenario's normal day, 120 s for mornings and 180 s for evenings, then applied it unchanged to the disturbed days. Same rule for my optimiser's settings: tuned on normal days only. Seeds are partitioned: tuning 100-109, evaluation 200-209, demo 300, forecaster history separate. Nothing was ever chosen on an evaluation seed. Common random numbers: the same seed means literally the same cars, same arrival times, same turns, for every controller. So differences between controllers are paired, which removes most of the day-to-day noise from the comparison. That's why 10 seeds is enough for clear intervals on normal days.

## Slide 10: Forecast arrivals at each entrance, 5 to 15 minutes ahead
2 · FORECASTER
SIMULATION
FORECASTER
OPTIMISER
RESULTS
Target and labels
The true arrival rate at each of the 8 entrances in the 5-min windows +5, +10 and +15 min ahead, issued every 5 minutes. One global model, horizon as a feature.
Labels are true rates (stand-in for a historical survey); inputs are only what is visible at time t.
Data and validation
60 simulated days (05:00–21:00) under the 60 s plan. Split by whole days in time order: 40 train / 10 validation / 10 test, plus 10 fresh days never used for any decision. 33 events in all (10 / 8 / 7 / 8).
Whole days, not random rows: neighbouring windows are autocorrelated, so random splits leak.
Features (all available at time t; tested to use the past only)
Group | Features | Captures
Clock | sin / cos harmonics of the hour being forecast, × entry; weekday / weekend; horizon | The daily profile and tide, per entrance
Live counts | Last six 5-min counts, their 30-min mean, network total | Today's level and timing shift (nowcast)
Weather | Rain now; noisy rain forecast for the window | Rain's +10% demand
Event calendar | log(1 + announced extra demand) now and in the target window; recent calendar values | Scheduled surges, before the cars arrive
Excluded (tested) | True rate now, road occupancy, queues, the real crowd size | Would be leakage or unavailable sensors
Censoring guard
When an entry road is estimated full (≥ 55 of ~61 cars) in the last 15 minutes, its counter is measuring the blockage, not the demand. The forecast then falls back to profile × a level multiplier built from clean data × the calendar.
Notes: The forecasting job: for each of the 8 entrances, predict the arrival rate 5, 10 and 15 minutes ahead, every 5 minutes. One global model with horizon as a feature, rather than 24 separate models, so the data is pooled. Labels versus inputs: this was my first mistake and I'll come back to it. The labels are the true rates, which in real life would come from a historical survey. The inputs are only what a deployed system could see at that moment. Tests check that no feature uses the future and that the oracle columns and occupancy are never features. Validation is by whole days in time order. Five-minute windows next to each other are strongly correlated; a random split would put 07:40 in training and 07:45 in test and flatter every model. The censoring guard: when an entry road fills, cars queue outside and the counter undercounts demand. The model would read that as low demand. So when the estimate says the road is nearly full, the forecast ignores that entry's counts.

## Slide 11: Why a Poisson GLM: it matches how the data is generated
2 · FORECASTER
SIMULATION
FORECASTER
OPTIMISER
RESULTS
Model | Why consider it | Error (all) | Error (events) | Verdict
Raw count carried forward | Naive benchmark | 24.0% | – | A 5-min count is mostly Poisson noise
Hour-of-day profile | The typical day | 10.4% | 40.4% | Misses today's level, shift and events
Profile × rain × event calendar | Patterns only, no live counts | 9.7% | 18.4% | Calendar alone halves event error
Poisson GLM + live counts + guard | Counts; log link = multiplicative effects | 7.1% | 13.3% | Chosen
Gradient boosting (Poisson loss) + counts + guard | Flexible check for missed interactions | 7.3% | 20.6% | Level overall, worse on rare events
Deep sequence models (LSTM, transformers) | Popular for traffic | not fitted |  | 60 days × 8 entries; structure known; boosting found nothing more
Error = mean absolute error as % of the mean true rate, 20 held-out days (test + fresh), averaged over +5/+10/+15 min. Events: 5 min ahead, event windows only.
Why a GLM
Counts → Poisson likelihood. Demand is a product of effects → log link makes them additive. With the calendar entered as log(1 + announced), a coefficient of 1 reproduces the event multiplier exactly, so the model can carry over to an event it has never seen.
Why not boosting
Same accuracy on normal days. On events it is clearly worse: with only 18 events in train + validation, trees with 200-row minimum leaves cannot learn a rare situation; a multiplicative term can.
Selection was light: GLM regularisation from 3 values, 4 boosting settings, picked on validation days.
Notes: The model-selection slide. I built a ladder from naive to flexible. The raw count carried forward is the worst, 24%, because a single five-minute count is mostly Poisson noise. The hour-of-day profile gets to 10%. Adding weather and the event calendar gets to 9.7% overall and halves the error on event days. The Poisson GLM with live counts gets 7.1%. Why a GLM: the data are counts, so Poisson likelihood; the demand is a product of effects, so a log link turns them into a sum. And the calendar feature log(1+announced) means a coefficient of one reproduces the event multiplier, so it extrapolates to new events. Gradient boosting is my flexibility check: it's level overall, 7.3%, so there's no structure the GLM is missing. But it's much worse on events, 20.6 vs 13.3, because events are rare: trees can't learn from 18 examples. I didn't fit deep models: 60 days of data, a known structure, and the flexible check already found nothing. I'd say that rather than claim I tried everything.

## Slide 12: A good nowcast, and the calendar predicts event surges
2 · FORECASTER
SIMULATION
FORECASTER
OPTIMISER
RESULTS
Error by horizon, % of mean true rate (20 held-out days)
Model | +5 min | +10 min | +15 min | All
Raw count carried forward | 23.0 | 23.9 | 25.1 | 24.0
Hour-of-day profile | 10.5 | 10.4 | 10.2 | 10.4
+ weather and event calendar | 9.9 | 9.7 | 9.6 | 9.7
Poisson GLM + live counts + guard | 6.7 | 7.0 | 7.6 | 7.1
Gradient boosting + live counts + guard | 6.8 | 7.3 | 7.7 | 7.3
Oracle: true rate now, held flat | 4.7 | 7.7 | 10.2 | 7.6
Nowcast: live counts cut the profile's error by a third: they reveal today's level and shift.
Shape: the oracle knows today's rate exactly but holds it flat; it wins only at +5 min. From +10 min the model's knowledge of the daily shape and calendar wins.
What's left is today's random variation and the gap between announced and actual crowds (sd 25%): nothing in the inputs predicts it.
Chart: Error by day type, 5 min ahead (%)
| Dry weekday | Rain | Accident | Event | Weekend
Hour-of-day profile | 9.9 | 10.5 | 11 | 40.4 | 9.1
Profile × rain × calendar | 9.5 | 8.9 | 10.6 | 18.4 | 9.9
GLM + counts + guard | 7 | 7.8 | 7.3 | 13.3 | 6.7
Boosting + counts + guard | 6.9 | 9.7 | 7.8 | 20.6 | 6.6
Notes: Two results. Left: error by horizon. The GLM beats the profile by about a third at every horizon. The interesting comparison is the oracle: it knows today's true rate exactly but assumes it stays flat. It wins at five minutes, and from ten minutes my model wins, because the model knows the daily shape (the rush is still ramping up) and the calendar. So the model's skill is mostly a good nowcast, plus the daily shape, plus the calendar. What's left is random variation that nothing in the inputs can see. Right: error by day type. On normal days every live-count model is around 7%. On event days the profile is 40% wrong; the calendar alone gets to 18%, and the GLM with counts and calendar to 13%. Boosting is 21% there, which is the strongest evidence for the GLM. Keep in mind for later: a good forecast is not the same as a forecast that improves control.

## Slide 13: Mistakes found in validation, and what changed
2 · FORECASTER
SIMULATION
FORECASTER
OPTIMISER
RESULTS
1 · Labels vs inputs mixed up
The first design blurred “trained on the true rate” and “trained on observed counts”. Now explicit: labels = true rate (a survey stand-in, only possible in a simulator), inputs = what a deployed system sees. Tests forbid oracle columns as features.
2 · Censoring broke every model
On one test day the grid gridlocked; entry counters reported the blockage and every learned model collapsed. Fix: the censoring guard (threshold from the road's capacity), confirmed on fresh days: 7.1% vs 8.7% unguarded (fresh), 7.0% vs 10.6% (test).
3 · Fewer sensors, same accuracy
An earlier version also read whole-road occupancy. Removing it changed nothing (6.82% before and after, measured before events were added), so the forecaster uses entrance counts only, consistent with the controller.
4 · Scoring against sensors hides skill
Scored against noisy counts, every model lands within ~1.3 points of the others: Poisson noise dominates. Against the true rate they separate clearly. Both are reported; decisions use the true rate.
Notes: Four things validation caught. I think these matter more than the headline error. One: I initially conflated training on true rates with training on counts. Now the rule is explicit and tested. Two, the most important: censoring. On one test day the network gridlocked, the counters reported the jam rather than the demand, and every model collapsed. The guard fixes it, and I confirmed it on fresh days I hadn't looked at. Three: I removed occupancy sensors from the forecaster and nothing changed, so I kept the simpler sensor set. Four: if you score against the noisy counts, every model looks the same because Poisson noise dominates. Score against the true rate and they separate.

## Slide 14: Control on four timescales
3 · OPTIMISER
SIMULATION
FORECASTER
OPTIMISER
RESULTS
Every | Layer | Does | Uses
1 s | Estimate | Advance the queue model on the entrance counts and own signals | Counts, own signal state
1 s | Execute | Switch when the planned green has run out; gap-out when the model says the approach is empty | The estimate
60 s | Plan | Webster cycle; convex QP for the green splits over the next 15 min; apply the first minute | Forecast + estimate
Day | Learn | Refit the forecaster on history | History
Why re-plan every 60 s?
Decisions are cycle-scale (cycles 40–120 s). Faster re-planning chases Poisson noise in the counts; the 1 s layer already reacts to individual cars. Slower re-planning misses ramps and incidents.
Why a 15-minute horizon?
Long enough for queues to propagate across the grid (a car crosses it in under 2 min, a queue builds over 5–10), and it matches the forecaster's horizon. The terminal cost covers what lies beyond.
Receding horizon
Plan 15 minutes, apply 1, re-plan from the new estimate and forecast. Model error and forecast error are corrected every minute: the plan never runs open-loop for long.
Notes: The controller works on four timescales. Every second it updates its queue estimate and executes the signals. Every 60 seconds it re-plans. Once a day the forecaster is refit. Why 60 seconds? The decision is a green split, which only means something at cycle scale. Re-planning every few seconds would chase Poisson noise. The second-by-second layer, gap-out, handles individual cars. Why 15 minutes? Long enough for a queue on one road to affect its neighbours, and the same horizon the forecaster predicts. The terminal cost stops the plan from pushing work past the horizon. It's receding-horizon control, MPC: plan 15 minutes, apply one, re-plan. That's what makes it robust to the forecast being wrong.

## Slide 15: Queue estimator: the controller's picture of the network
3 · OPTIMISER
SIMULATION
FORECASTER
OPTIMISER
RESULTS
Store-and-forward model, the same one the optimiser plans with, stepped every second.
Each road: a travel-time delay line (cars driving to the stop line at free speed) and a stop-line queue.
Entry roads gain the counter increments. A green, unblocked road discharges min(queue, saturation flow × 1 s), split downstream by the average turn shares. Queues above a road's storage are handed back to its feeders (spillback).
Calibrated, not tuned: discharge rate 0.95 × nominal (rain-adjusted) and a 1 s start-up delay were fitted by replaying tuning-seed runs against the simulator's truth, not chosen to lower delay.
Accuracy against the simulator's truth (tuning seeds)
Day | Estimate error | Verdict
Typical morning | Entry 0.3–0.4 cars, internal 1.2 (true ~6, ~4) | Good
Storm | Total 2–8 cars high on average, peaks 70–80 (of ~140) | Drifts
After an accident | Assumes the backlog drains at full rate: up to 280 low | Wrong → fallback
Event surge | Assumes full entry roads keep draining; counters go quiet | Wrong on bad days
Notes: With counts only, the controller has to estimate the queues. It uses the same store-and-forward model the optimiser plans with, stepped every second. Cars enter on the counted roads, drive to the stop line at free speed, queue, and leave at saturation flow when green, splitting by the average turning shares. The two parameters, discharge rate and start-up delay, were calibrated against the simulator's truth on tuning seeds. They were not tuned for delay, which would be overfitting. How good is it? The figure: on a normal morning the blue estimate tracks the black truth closely; entry roads within half a car. In the accident panels, it tracks the blockage via the incident feed, but after clearance it thinks the backlog drains at full saturation, when really spillback holds it longer. So it reads too low. That's why the incident fallback exists. The same failure appears in the stadium event, triggered by demand rather than a blockage: when entry roads fill, cars wait outside, the counters go quiet, and the estimator thinks the road is emptying. No sensor inside the network corrects it, and that's the single biggest limitation.

## Slide 16: The optimisation: a convex quadratic program, solved every minute
3 · OPTIMISER
SIMULATION
FORECASTER
OPTIMISER
RESULTS
decide x[i,k] NS green share at junction i, minute k
(EW share = 1 − x), k = 1..15
state q[l,k+1] = q[l,k] + a[l,k] − u[l,k]
q[l,0] = the estimator's cars now
arrive a[l,k] = forecast λₑ·60 on entry roads
= T · u[k−1] on internal roads (turn shares)
serve u[l,k] ≤ s · 60 · g_l(x[i,k]) g = x − L/C or 1 − x − L/C
u[l,k] ≤ q[l,k] + a[l,k]; u = 0 on a blocked road
bounds x_lo ≤ x ≤ x_hi (green 8–60 s, 4 s lost, at cycle C)
store q[l,k] ≤ storage_l + slack[l,k]
min Σq + 0.3·Σq² + 3·Σq_end + 5·Σslack + 2·Σ|Δx|
Objective term | Role
Σq | Cars waiting × minutes = total delay (Little's law)
0.3 Σq² | Fairness: spreads queues, stops starving light approaches
3 Σq_end | Terminal cost: no dumping work past the horizon
5 Σslack | Soft storage limit: prices spillback, keeps it feasible
2 Σ¦Δx¦ | Smoothness: plans don't flap minute to minute
Size and speed (2x2)
4 × 15 split variables, ~740 flow, queue and slack variables. Clarabel interior point via CVXPY: 38 ms mean, 42 ms max.
Cycle length C sits outside the program
Webster: C = (1.5·L + 5) / (1 − Y), L = 12 s, Y = busiest junction's critical flow ratio from the forecast. Smoothed 40% per decision toward its target, rounded to 5 s, clamped 40–120 s. Inside the QP, green = x·C would be bilinear (non-convex).
Notes: This is the formulation. For each junction and each minute in the next 15, decide the north-south share of green. Queues evolve by conservation: queue next minute equals queue now plus arrivals minus departures. Arrivals on entry roads come from the forecast; on internal roads they're last minute's departures upstream times the turning shares. Departures are capped by saturation flow times green time, and by what's there. A blocked road discharges nothing. The objective: sum of queues over time is total delay in vehicle-minutes, by Little's law. The quadratic term is the fairness term: it penalises long queues more than proportionally, so the optimiser can't starve the light approaches to serve the heavy ones. Terminal cost, spillback slack, and a smoothness penalty. All constraints are linear and the objective is convex quadratic, so it's a QP: globally optimal, solved in about 40 ms. The cycle length is set outside, by Webster's formula. If C were a variable, green time would be x times C, a product of variables, and the problem would be non-convex. Webster is the textbook delay-minimising cycle for given flows, and it uses the forecast.

## Slide 17: Why this formulation, and not the alternatives
3 · OPTIMISER
SIMULATION
FORECASTER
OPTIMISER
RESULTS
Alternative | What it would buy | Why not here
Linear program (drop q²) | Slightly faster; still exact | Corner solutions: all spare green to one approach, starving the light side. Speed isn't binding: 38 ms vs a 60 s budget.
Mixed-integer phase sequencing | Phase order, skipping, offsets | Two-phase junctions have no order to choose; splits are continuous. Exponential cost for no gain.
Cycle length as a decision variable | Joint optimum of C and splits | Green = x·C is bilinear → non-convex, local optima. Webster outside + smoothing is the standard decomposition.
Nonlinear / simulation-based optimisation | Uses the real dynamics | Slow, no optimality certificate, and it would optimise inside the evaluator.
Max-pressure (Varaiya 2013) | Simple, stable, no forecast needed | Myopic; maximises throughput not delay. With true queues (camera version) it lost to the optimiser everywhere and to the tuned plan in 4 of 5 scenarios.
Reinforcement learning | No model needed | Needs thousands of simulated days, opaque, no guarantee; we already know the structure.
Webster / fixed-time only | Robust, no state needed | That is the tuned baseline, which the optimiser beats in 6 of 6 scenarios.
Convex: local optimum = global
Every solve returns the optimum of its model, with a certificate. Remaining error is in the model's inputs (forecast, estimate), not in the search.
Is a simpler method faster?
Yes, but speed is not the constraint: 38 ms per decision on 2x2, 1.9 s on 10x10, against 60 s. Convexity is what matters: it keeps the solve exact and explainable.
Notes: The "why X over Y" slide for the optimiser. Why not an LP? It would be convex too and a bit faster, but LPs land on vertices: give all the spare green to one approach. The quadratic term gives smooth, fair splits. And speed isn't the constraint: 40 ms against a 60 second budget. Why not a mixed-integer formulation? That's for choosing phase orders or offsets. With two phases there's nothing discrete to choose. Why not put the cycle in the program? Bilinear, non-convex. Webster outside is the standard decomposition. Max-pressure is the famous alternative. I ran it in the camera version where it had the true queues: it lost to the optimiser everywhere and to the tuned fixed plan in four of five scenarios. It's designed for stability at max throughput, not minimum delay, and it has no look-ahead, so a forecast is useless to it. That's why it didn't fit this project's theme either. RL: possible, but data-hungry and opaque, and the structure is known. I'd rather use the model. The point of convexity: local optimum is global, so any remaining error is in the inputs, not the solver.

## Slide 18: Gap-out, the incident fallback, and a bug found late
3 · OPTIMISER
SIMULATION
FORECASTER
OPTIMISER
RESULTS
Gap-out (every second)
End a green early when the estimate says fewer than 0.5 cars are due at its stop lines within 4 s, and the cross street has at least one.
Typical morning, seeds 200–202:
Tuned fixed 59.9 s
QP alone 52.8 s (−12%)
QP + gap-out 42.0 s (−30%)
In light traffic most of the gain is this reactive layer acting on the queue model; at the busy peak the QP does most of the work.
Incident fallback
From the incident report until 60 min after clearance, run the tuned 120 s green wave. After a blockage the estimate is known to be wrong, so a robust plan beats optimising on a wrong state.
Accident, 10 held-out seeds:
With fallback 225 s, 0 gridlocks
No incident feed 457 s, 2 gridlocks
Window chosen on accident tuning seeds 100–109: fallback only while blocked was worse; 15/30/45/60 min after clearance improved in that order.
Bug: the cycle never moved
Reviewing the demo, the cycle barely ever changed.
C ← round((0.6 C + 0.4 C*) / 5) · 5
Rounding the smoothed state every minute stalls it one 5 s step short of its target: it could never leave 45–115 s. Fix: keep the smoothed value unrounded, round only what is executed. Test added; every result rerun.
Effect: storm 12% → 15%, event 5% worse → 5% better.
Notes: Three practical pieces. Gap-out: if the estimate says nobody is arriving on the green approach and someone is waiting on the cross street, end the green early. This turned out to be a big part of the gain in light traffic: the QP alone is 12% better than tuned on a typical morning; with gap-out it's 30%. That's honest attribution: in light traffic, the reactive layer matters; at peak the QP matters. Incident fallback: when the incident feed reports a blockage, the signals switch to the tuned fixed plan until an hour after it clears. That sounds like giving up, but the estimate is wrong after a blockage and a robust plan beats optimising on a wrong state. Without the incident feed the counts-only controller gridlocks two of ten accident days. The window was chosen on tuning seeds. And a bug, which I want to own: the cycle smoothing rounded its own state every step, so it got stuck one step short of the target and essentially never moved. Found while reviewing the demo, fixed, test added, and every result in this deck is from the rerun. It mattered most in the storm and the event, where the cycle should move.

## Slide 19: Same traffic, two controllers, side by side
LIVE DEMO
1
Normal hour
Gap-out keeps light approaches moving
2
Morning peak
Splits follow the tide; cycle grows
3
Storm
Saturation flow falls; estimate drifts high
4
Accident
Incident feed → fallback plan
5
Stadium event
Calendar sees the surge; estimate struggles
What to watch
Left vs right: tuned fixed plan vs optimiser on identical cars (same seed).
Estimate vs truth: the controller's cars per road next to the real count it never sees.
Plan: current NS share and cycle at each junction.
Forecast chart: counted arrivals, the forecast, and the true demand (hidden from the controller); event window shaded.
Honest clip selection
Windows chosen by a rule: the worst quarter-hour for the fixed plan across held-out seeds (for the event, its first quarter-hour). Each clip is one random day (seed 300); the viewer shows the held-out average beside it.
outputs/demo_viewer.html
Notes: Switch to the browser: outputs/demo_viewer.html. Deep link format #clip=3&f=600. Suggested order (about 5 minutes): 1. Morning peak: point out estimate vs truth bars, the plan, and that the cycle now moves. 2. Accident: the incident banner, the fallback to the fixed plan, the backlog clearing. 3. Stadium event: the shaded calendar window, the forecast rising before the counts, and the eastbound entries filling. 4. If time: storm, the estimate running high. Mention the clip rule: I didn't pick flattering windows; the rule picks the fixed plan's worst quarter-hour. One day can look better or worse than average; the held-out average is shown next to it.

## Slide 20: Held-out: ahead of the tuned plan in all six scenarios, by 5–32%
4 · RESULTS
SIMULATION
FORECASTER
OPTIMISER
RESULTS
Chart: Mean delay per car (s), held-out seeds
| Typical AM | Busy AM | Storm | Evening | Accident | Stadium event
Fixed 60 s (untuned) | 114.1 | 265.5 | 294.7 | 238.7 | 417.1 | 314.2
Fixed, tuned green wave | 72.2 | 142.1 | 199.6 | 100.1 | 242.1 | 138.6
Optimiser, live forecast | 49.4 | 110.7 | 169.1 | 86.2 | 225 | 132.3
vs tuned plan | Saving | s saved, 95% CI | n
Typical morning | 32% | 22.8 ± 4.0 | 10
Busy morning | 22% | 31.4 ± 28.8 | 3
Storm | 15% | 30.5 ± 11.2 | 3
Evening | 14% | 13.8 ± 3.7 | 10
Accident | 7% | 17.1 ± 18.3 | 10
Stadium event | 5% | 6.3 ± 19.3 | 10
vs the untuned 60 s plan: 43–64% better everywhere.
Clearly significant: typical, storm, evening; busy only just (3 seeds). Accident and event: not significant.
Tail (p95) better on typical (216 → 145 s), busy, storm, accident; level in the evening and event.
Throughput unchanged: every controller clears the same demand.
Notes: The headline chart, on held-out seeds the controller never saw. Grey: untuned 60 s. Dark: tuned green wave. Amber: the optimiser. Against the untuned plan, 43 to 64 percent everywhere. Against the tuned plan, 32 percent on a typical morning, 22 on a busy one, 14-15 in the storm and evening, and 5-7 in the accident and event. Statistics: paired by seed thanks to common random numbers, 95% t-intervals on the saving. Typical, storm and evening clearly exclude zero. Busy only just, with 3 seeds. Accident and event do not: the day-to-day swing is large. Tail delay: better in four scenarios, level in evening and event. The optimiser lowers the mean by serving heavy approaches; the q-squared term limits how much the light side pays. So the 20% target: met against untuned everywhere; against a strong tuned baseline, met on the mornings. I'd argue real fixed plans are rarely tuned per scenario like this.

## Slide 21: Value of information: the forecast is not what drives the gain
4 · RESULTS
SIMULATION
FORECASTER
OPTIMISER
RESULTS
Forecast given to the same optimiser | Typical | Busy | Storm | Evening | Accident | Event
Repeat the last window's count (persistence) | 49.2 | 109.3 | 162.8 | 84.7 | 226.9 | 135.4
Calendar + weather only (patterns) | 49.3 | 120.3 | 179.1 | 88.9 | 230.1 | 130.1
Live forecast (the model) | 49.4 | 110.7 | 169.1 | 86.2 | 225.0 | 132.3
Perfect forecast (oracle: the true rate) | 49.1 | 112.2 | 176.8 | 87.2 | 228.4 | 128.8
Tuned fixed plan, for reference | 72.2 | 142.1 | 199.6 | 100.1 | 242.1 | 138.6
Why it doesn't matter (normal days)
At a 15-minute horizon the forecast's value is mostly “today's level now”, and the controller re-plans every minute from counts that already carry it. A perfect forecast is within noise of persistence.
The event: where it should matter
The calendar tells the forecaster about the crowd before it arrives, and the forecast is right (13% vs 40% error). The perfect forecast is the best event row, by 7 s out of 130 with a ±19 s spread: not significant.
Where the gain actually is
The queue model, gap-out and the optimiser. In a surge the limit is the queue estimate, not the arrivals forecast. The next improvement is a measurement of the queues, not a better model.
Notes: This is the most important slide for the ML section, and I'd rather say it than have you find it. I ran the same optimiser with four levels of information: repeat the last count, calendar and weather only, my learned forecast, and a perfect oracle. The delays are within noise of each other, in every scenario. Even a perfect forecast doesn't help. Why? The optimiser re-plans every minute. The live counts already tell it today's level. Over 15 minutes, today's level is most of what a forecast knows. And the receding horizon corrects forecast error every minute. So I added the stadium event, the case where information should arrive before the cars: the calendar. The forecaster does see it coming, and the perfect forecast is the best row, but by 7 seconds with a 19-second spread. The conclusion I'd defend: the ML is good and correctly validated, but for this control problem, at this horizon, the binding constraint is state estimation, not prediction. That's a finding, not a failure. If asked "so why have the forecaster?": Webster's cycle and the QP's arrivals need a rate; the GLM is the right way to produce one; it's what would matter at longer horizons or for planning; and the experiment that tells you it doesn't matter here needed it built.

## Slide 22: Accident and stadium event: where counts-only runs out
4 · RESULTS
SIMULATION
FORECASTER
OPTIMISER
RESULTS
Accident: one lane blocked 15 min at the peak (10 seeds)
Controller | Normal day | With accident | Cost | Worst seed
Fixed 60 s (untuned) | 114.1 | 417.1 | +303 | 1189 (gridlock)
Fixed, tuned (120 s) | 72.2 | 242.1 | +170 | 400
Optimiser + fallback | 49.4 | 225.0 | +176 | 311
Optimiser, no incident feed | – | 456.5 | – | 1165 (2 gridlocks)
The accident adds ~170–180 s per car under any controller that keeps moving: there is no rerouting, so cars wait for it to clear.
The optimiser wins the day (7%, n.s.) because it is ahead before the accident; the accident itself costs it slightly more.
The incident feed is essential: without it, two of ten days gridlock.
Stadium event: two entries double for 45 min (10 seeds)
Controller | Normal evening | With event | Cost | Range
Fixed 60 s (untuned) | 238.7 | 314.2 | +76 | 214–440
Fixed, tuned (180 s) | 100.1 | 138.6 | +39 | 100–179
Optimiser, live forecast | 86.2 | 132.3 | +46 | 83–217
Ahead on 9 of 10 seeds (by 2–24 s), but one seed (207) goes badly: 217 s vs 149 s.
The forecast was right: at 16:10 it predicted 685 cars/h on the eastbound entries vs 392 at the time.
The estimate fails: when roads downstream fill, it still assumes full entry roads drain at saturation, and counters go quiet as cars queue outside. It sees an empty approach and starves it: the accident's failure mode, caused by demand.
Raising the cycle cap to 180 s made both evening and event worse (tuning seeds); not adopted.
Notes: The two disturbance scenarios, where counts-only shows its limits. Accident: the blockage adds about 170-180 seconds per car whatever you do, because cars behind a blocked single lane wait for it to clear and there's no rerouting. No signal plan fixes that. The optimiser wins the day because it was ahead before; the accident itself costs it about the same as the fixed plan. Without the incident feed it can't know the road is blocked and gridlocks twice in ten. Event: the optimiser is ahead on nine of ten days, but one day goes badly. I traced it: the forecaster saw the surge coming from the calendar. What failed is the estimate: entry roads fill, cars queue outside the boundary, the counters go quiet, and the estimator, which assumes queues drain at saturation, thinks the approach is emptying. The optimiser then gives that approach less green: exactly the wrong move. On seed 207, the two controllers that use live counts blow up, and the calendar-only and perfect ones don't, which fits the quiet-counter story. Fixes I'd build next: treat an entry road as full when its counter goes quiet while the calendar says a crowd is coming, or a calendar-triggered fallback like the accident's. I didn't build them, because the event was added after everything was frozen and I didn't want to tune on it.

## Slide 23: Scalability and engineering
4 · RESULTS
SIMULATION
FORECASTER
OPTIMISER
RESULTS
Chart: QP solve time vs intersections (one central solve)
| 4 | 16 | 36 | 100
Mean solve time (ms) | 38 | 203 | 512 | 1857
Grid | Junctions | Mean / max solve | Delay: untuned fixed vs optimiser
2x2 | 4 | 38 / 42 ms | 45 vs 37 s
4x4 | 16 | 203 / 254 ms | 79 vs 74 s
6x6 | 36 | 512 / 591 ms | 109 vs 103 s
10x10 | 100 | 1.9 / 2.4 s | 147 vs 132 s
~19 ms per junction against a 60 s budget. Larger grids use the persistence forecast (the GLM is fitted to the 2x2's entries); one seed, 20 min, untuned.
33 tests (pytest, ~20 s)
Simulator: conservation, no overlap, saturation flow, rain, accident, events, reproducibility, common random numbers.
Forecaster: past-only features, no oracle or occupancy columns, whole-day splits, censoring guard.
Optimiser: counts-only observation, bounds hold, splits follow demand, blocked roads get no green, cycle smoothing reaches both caps, fallback window.
Code and reproducibility
src/traffic: simulator, demand, scenarios; controllers (fixed, optimiser); forecasting; experiments; viz.
Every grid is generated from rows × cols: 10x10 is a config change.
Every number in this deck regenerates from the README Setup commands; long runs are chunked and resumable; seeds are fixed.
Controller registry: new controllers plug in with one class.
Notes: Scalability: the same code runs on any grid. One central QP per decision grows roughly linearly, about 19 ms per junction; 100 junctions take under 2 seconds against a 60 second decision interval. Beyond that you'd decompose by region, which the store-and-forward structure allows. On the larger grids the optimiser still beats the untuned plan, without any tuning. Engineering: 33 tests, running in about 20 seconds. The ones I'd point to are the guard-rail tests: features use the past only, no oracle columns, and the controller can only read the allowed sensors. Those protect the experiment's validity, not just the code. Reproducibility: fixed seeds, common random numbers, and every number in the deck comes from a command in the README.

## Slide 24: Limitations, stated plainly, and what I would do next
WRAP-UP
SIMULATION
FORECASTER
OPTIMISER
RESULTS
Limitations
The forecast adds little to control, even in the event it predicts well. Against the brief's expectation that ML drives the gain.
20% vs the tuned plan only on the mornings; storm 15%, evening 14%, accident and event not significant.
The queue estimate has no correction from inside the network: it drifts in storms and fails after accidents and in event surges.
Synthetic data: the forecaster recovers a process I wrote; rates of rain, accidents and events are assumptions.
Simplified network: one lane, two phases, no rerouting, no pedestrians; offsets not optimised.
Few seeds for busy and storm (3), so wide intervals.
Next steps, by expected value
1. A stop-line counter per road: corrects the estimate directly; attacks the main error source.
2. Detect full entry roads: a counter that goes quiet while the calendar says a crowd is coming → treat the road as full, or a calendar-triggered fallback.
3. Robust optimisation over forecast and estimate uncertainty (scenario or chance-constrained QP).
4. More seeds for busy and storm; tuning on disturbed days.
5. Coordination offsets chosen by the optimiser; rerouting in the simulator.
6. Real data: calibrate demand and saturation flow on a city's loop-detector feed.
Notes: Limitations, plainly. The forecast adds little to control. 20% against the tuned plan only on mornings. The estimate is the weak spot. The data is synthetic. The network is simplified. And busy and storm have only three seeds. Next steps in order of expected value. The biggest is a measurement inside the network: a stop-line counter on each road would let the estimator correct itself, which addresses the storm, the accident and the event at once. Second, use the information I already have better: a silent counter plus a calendar event means a full road. Third, plan robustly over the uncertainty in the estimate. Then more seeds, offsets, rerouting, and real data. Notice that a better forecaster isn't on the list. The experiments say that's not where the gain is.

## Slide 25: What I'd want you to remember
SUMMARY
Simulation
A vehicle-level simulator that is richer than the controller's model, so results include model error. Counts-only sensing, enforced by tests.
ML
A Poisson GLM matched to the data: 7.1% error, a third better than the profile, and it predicts event surges from the calendar. Validated on whole held-out days; censoring caught and fixed.
Optimisation
A convex QP on a store-and-forward model, Webster cycle outside, receding horizon, gap-out and an incident fallback. 38 ms per solve; 1.9 s at 100 junctions.
Result
32% less delay than a tuned fixed plan on a normal morning, 43–64% vs untuned, ahead in all six scenarios. The gain comes from the queue model, not the forecast; next is a queue sensor.
Notes: Four things to remember. A simulator I didn't let the controller grade itself in. A forecaster chosen to match the data and validated properly. A convex optimiser that is fast, exact and explainable. And a result that's strong on normal days, honest about where it isn't, and clear about what to build next. Then open to questions.

## Slide 26: Intelligent Driver Model and saturation flow
BACKUP
dv/dt = a · [ 1 − (v / v₀)⁴ − (s* / s)² ]
s* = s₀ + v·T + v·Δv / (2·√(a·b))
ballistic update, Δt = 0.5 s; red light = a stopped virtual car at the stop line
Parameter | Dry | Full rain
Free speed v₀ | 13.9 m/s | −20%
Time headway T | 1.5 s | +30%
Max acceleration a | 1.5 m/s² | −15%
Comfortable braking b | 2.0 m/s² | 
Standstill gap s₀ / car length | 2 m / 4.5 m | 
Measured saturation flow | 0.40 veh/s (2.5 s headway) | 0.33 veh/s
Why it matters
Saturation flow is the single most important number for both the estimator and the QP. Because it emerges from IDM, the controller's nominal value (0.40, −17.5% in rain) is a calibrated estimate of the simulator, not the simulator's own parameter; there is genuine model error.
Dilemma-zone rule: at amber, a car that cannot stop with braking ≤ 4.5 m/s² continues through (Gazis, Herman & Maradudin 1960).
Tested: saturation flow matches config; rain cuts it.
Notes: Backup for "how does the car-following work". IDM: acceleration is a free-road term minus an interaction term based on the desired gap s-star. A red light is modelled as a stopped car at the stop line. Saturation flow emerges at about 2.5 s headway; I measured it and a test checks it.

## Slide 27: Webster's cycle and the cap check
BACKUP
C* = (1.5·L + 5) / (1 − Y)
Y = max over junctions of y_NS + y_EW, y = q / s
L = 12 s effective lost time per cycle
Webster (1958): the cycle that minimises average delay at an isolated junction for given flows. Y from the forecast flows.
Smoothed: C_s ← 0.6·C_s + 0.4·C*; executed C = round(C_s / 5)·5, clamped to 40–120 s.
Why outside the QP: green = share × C is bilinear; fixing C per decision keeps the QP convex.
Cycle cap 120 vs 180 s (tuning seeds 100–104)
Forecast | Evening, cap 120 | Evening, cap 180 | Event, cap 120 | Event, cap 180
Persistence | 110.3 | 127.9 | 169.5 | 184.8
Live | 107.2 | 129.0 | 174.2 | 185.2
Perfect | 112.0 | 131.2 | 178.9 | 189.0
Tuned fixed (180 s) | 124.1 |  | 175.8 | 
The tuned evening plan uses 180 s, so a 180 s cap was the natural question. It is worse in both scenarios: the 120 s cap stays.
Notes: Backup on the cycle. Webster's formula, and the cap check: since the tuned evening plan uses 180 seconds, I checked whether the optimiser should be allowed 180. On tuning seeds it's worse in both the normal evening and the event, so the cap stays at 120.

## Slide 28: Optimiser settings: one-at-a-time check on tuning seeds
BACKUP
Change from defaults | Typical morning (s) | Evening (s) | Score (mean) | p95 (s)
Defaults | 46.6 | 110.3 | 78.5 | 254
Switching weight 0.5 / 5.0 (default 2) | 45.7 / 46.8 | 112.0 / 107.7 | 78.8 / 77.3 | 263 / 256
Quadratic weight 1 / 10 (default 3) | 46.2 / 46.9 | 111.4 / 108.4 | 78.8 / 77.6 | 257 / 248
Terminal weight 1 / 6 (default 3) | 47.0 / 46.6 | 110.3 / 111.4 | 78.7 / 79.0 | 257 / 263
Webster lost time 8 / 16 s (default 12) | 45.9 / 46.1 | 110.7 / 109.6 | 78.3 / 77.9 | 255 / 254
Gap-out off | 56.7 | 118.3 | 87.5 | 271
Gap-out window 2 / 8 s (default 4) | 45.2 / 53.0 | 107.8 / 113.8 | 76.5 / 83.4 | 251 / 254
Everything lands within ~2 s of the defaults except gap-out (off: +9 s). The surface is flat, so the defaults were kept rather than chasing tuning-seed noise.
Weights are in “cars” units: the quadratic term is divided by 10 inside the program (0.3 per car² per minute).
Source: outputs/sweep_summary.csv (scripts/sweep.py).
Notes: Backup for "how did you choose the weights". One at a time around the defaults on tuning seeds. It's flat: nothing moves more than about 2 seconds except gap-out. A flat surface means the result is not a product of lucky tuning.

## Slide 29: Earlier camera version and max-pressure (seeds 200–202)
BACKUP
Controller (mean delay per car, s) | Typical | Busy | Storm | Evening | Accident
Fixed, tuned green wave | 59.9 | 142.1 | 199.6 | 95.0 | 199.8
Max-pressure (true queues from cameras) | 58.3 | 177.7 | 229.7 | 137.3 | 243.7
Optimiser (true queues from cameras) | 46.5 | 111.3 | 167.7 | 91.7 | 206.6
Optimiser (counts only, this version) | 42.0 | 110.7 | 169.1 | 83.2 | 190.7
Max-pressure: each moment, green goes to the phase with the largest (own queue − downstream queue). Throughput-optimal and stable, but myopic: it does not minimise delay and has no use for a forecast. With true queues it lost to the optimiser in every scenario and to the tuned plan in four of five.
Counts only cost nothing: the counts-only optimiser matches or beats the camera one, because model-based gap-out works on the estimate. The camera code has been replaced; these numbers are kept for reference.
Notes: Backup on max-pressure and the camera version. Max-pressure with perfect queue information still lost. Under counts only it would have to act second by second on the estimate, which is worse still. That plus no use for a forecast is why it was dropped.

## Slide 30: AI use
BACKUP
Anthropic's Claude (via Claude Code) was used throughout as a pair-programmer: it wrote or drafted most of the simulator, forecasting pipeline, optimiser, tests, viewer and README, working from the brief and my direction.
I set the framing and made the decisions: forecasting true rates rather than sensor counts, the counts-only sensing assumption, the time-stepped simulator, the headline baseline, the event experiment, and how the limits are presented.
I reviewed the outputs, and that is how problems were found: for example the cycle that never moved, spotted in the demo, traced to the smoothing code, fixed and rerun.
Every reported number comes from code in the repository; the held-out results regenerate from the README Setup commands; 33 tests guard the experiment's rules.
Notes: Backup for the AI question. The brief encourages it, as long as I can explain everything. Rewrite this slide in your own words before presenting.

## Slide 31: References
BACKUP
Simulation, signal control and optimisation
Treiber, Hennecke & Helbing (2000), Congested traffic states…, Phys. Rev. E 62(2); Treiber & Kesting (2013), Traffic Flow Dynamics, Springer
Gazis, Herman & Maradudin (1960), The problem of the amber signal light in traffic flow, Operations Research 8(1)
Law (2015), Simulation Modeling and Analysis, 5th ed., ch. 11 (common random numbers)
Webster (1958), Traffic Signal Settings, Road Research Technical Paper 39, HMSO
Gazis & Potts (1963), The oversaturated intersection; Aboudolas, Papageorgiou & Kosmatopoulos (2009), Transp. Res. C 17(2)
Mayne, Rawlings, Rao & Scokaert (2000), Constrained model predictive control, Automatica 36(6)
Varaiya (2013), Max pressure control of a network of signalized intersections, Transp. Res. C 36
Koonce et al. (2008), Traffic Signal Timing Manual, FHWA-HOP-08-024
Forecasting and software
Nelder & Wedderburn (1972), Generalized linear models, JRSS A 135(3)
Ke et al. (2017), LightGBM, NeurIPS 30 (scikit-learn's HistGradientBoosting follows it)
Hyndman & Athanasopoulos (2021), Forecasting: Principles and Practice, 3rd ed.
Diamond & Boyd (2016), CVXPY, JMLR 17(83)
Goulart & Chen (2024), Clarabel, arXiv:2405.12762
Pedregosa et al. (2011), Scikit-learn, JMLR 12
NumPy (Harris et al. 2020), SciPy (Virtanen et al. 2020), pandas, matplotlib
Notes: References for the methods used. The provided starter code was read but not used.